## Slide 1
Sequential Logic Circuits
Design and Simulation of a Smart Water Tank
Remembering & Keeping Time: Sequential Logic
Presented by: group-10
_______________
1

## Slide 2
The Big Idea: Sequential Logic
Connecting the smart water tank to the CPU memory-and-stepping concept
• Combinational logic produces outputs from present inputs only.
• Sequential logic adds memory: the circuit can remember a previous condition.
• A clock lets the system update its state in an organized, repeatable way.
• In a smart water tank, the controller remembers whether the tank is LOW, MEDIUM, or FULL.
• This same idea is used by CPUs to remember values and step through instructions.
2

## Slide 3
Why Does the Water Tank Need Memory?
Water-level sensors
Sequential controller
Pump
• If the tank is LOW, the pump should start filling it.
• If the tank is MEDIUM, the controller may keep the pump running.
• If the tank becomes FULL, the pump must stop.
• The controller therefore needs a stored state, not just a direct sensor-to-pump connection.
3

## Slide 4
System Specification
Input / Element | Meaning
L | LOW-level sensor
M | MEDIUM-level sensor
H | HIGH/FULL sensor
CLK | Clock signal
RESET | Initializes controller
PUMP | Pump control output
Goal Automatic filling
Safety Stop at FULL
Memory Store state
4

## Slide 5
Latches and Flip-Flops
SR Latch Basic memory element
D Latch Level-sensitive
D Flip-Flop Edge-triggered
• SR latch stores a bit using feedback.
• D latch follows the input while enabled and holds it when disabled.
• D flip-flop captures D at a clock edge and holds the captured value.
• For the smart water tank, D flip-flops are convenient for storing the FSM state.
5

## Slide 6
Clock and Synchronous Design
Sensor Inputs
Next-State Logic
D Flip-Flops
CLOCK
• All state elements update on a chosen clock edge.
• Clocking makes the controller's behavior easier to design and simulate.
• Setup time: inputs should be stable before the active edge.
• Hold time: inputs should remain stable briefly after the active edge.
6

## Slide 7
Registers: Storing Multi-Bit Values
DFF 1
DFF 2
DFF 3
DFF 4
A row of flip-flops forms a register
• In a CPU, registers store operands, addresses, and intermediate values.
• In our project, the state register stores the current water-tank state.
• Each flip-flop stores one bit of the state.
7

## Slide 8
Shift Registers — Brief Connection
1
0
1
1
• A shift register moves stored bits left or right on clock edges.
• Useful in serial communication, data transfer, delay lines, and temporary storage.
• The smart water tank mainly needs state storage, so a simple register/FSM is sufficient.
8

## Slide 9
Counters and the Program-Counter Pattern
Clock
Synchronous Counter
Count Value
Clock | Counter
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
• A synchronous counter changes its stored value on clock edges.
• A CPU's program counter follows this pattern: it stores which instruction is next.
• The water-tank controller also advances through defined states one clock at a time.
9

## Slide 10
Finite State Machine (FSM)
Present State
Next-State Logic
Next State
CLOCK
• An FSM describes step-by-step behavior using states and transitions.
• State transitions depend on inputs and the current state.
• An FSM is a common way to design the control unit of a digital system.
10

## Slide 11
Smart Water Tank FSM — State Diagram
S0
LOW
Pump ON
S1
MEDIUM
Pump ON
S2
FULL
Pump OFF
Rising
FULL
Water decreases → return toward S1/S0
11

## Slide 12
FSM State Table
Present State | Water Condition | Next State | Pump
S0 LOW | Low | S0 / S1 | ON
S1 MEDIUM | Medium | S1 | ON
S1 MEDIUM | Full | S2 | ON → OFF
S2 FULL | Full | S2 | OFF
S2 FULL | Water decreases | S1 | OFF → ON
• The exact sensor encoding can be adapted to the simulator used.
• A practical design can add hysteresis so the pump does not chatter around a boundary.
12

## Slide 13
State Encoding with D Flip-Flops
State | Q1 | Q0 | Pump
LOW | 0 | 0 | ON
MEDIUM | 0 | 1 | ON
FULL | 1 | 0 | OFF
Unused | 1 | 1 | —
Two D flip-flops store Q1 and Q0
D inputs = next-state values
Clock edge updates Q1 Q0
13

## Slide 14
Pump Control Logic
LOW 00 → ON
MEDIUM 01 → ON
FULL 10 → OFF
PUMP = Q1′
• When Q1 = 0, the stored state is LOW or MEDIUM → pump ON.
• When Q1 = 1 for the FULL state → pump OFF.
• The pump output in a real circuit should drive a suitable transistor/relay stage.
14

## Slide 15
Simulation Design
Sensors L / M / H
Next-State Logic
D Flip-Flops Q1 Q0
Pump LED / Driver
CLOCK
• Use switches to simulate sensor inputs.
• Use LEDs to display state and pump output.
• Apply RESET first, then change sensor conditions and observe state transitions at clock edges.
15

## Slide 16
Simulation Sequence / Expected Output
Clock | Water Level | State | Pump
0 | LOW | S0 | ON
1 | LOW | S0 | ON
2 | MEDIUM | S1 | ON
3 | MEDIUM | S1 | ON
4 | FULL | S2 | OFF
5 | FULL | S2 | OFF
6 | MEDIUM | S1 | ON
7 | LOW | S0 | ON
16

## Slide 17
Milestone: Working Sequential-Logic Fabric
1. Working Register Stores state
2. Counter Pattern Steps on clock
3. Working FSM Controls pump
• Register → remembers the tank state.
• Clock/counter pattern → provides controlled stepping.
• FSM → converts sensor conditions into state transitions.
• Together these form the memory-and-stepping fabric behind the automated controller.
Sensors → FSM → Flip-Flops → Pump
17

## Slide 18
Advantages, Applications & Limitations
Advantages
• Prevents overflow
• Reduces wastage
• Automatic pump control
• Less manual monitoring
Applications
• Homes
• Apartments
• Hospitals & hotels
• Industrial tanks
Limitations
• Sensor faults
• Clock-edge response
• Driver/isolation needed
• Placement affects accuracy
18

## Slide 19
Conclusion
Smart Water Tank = Sensors + Memory + Clock + FSM + Pump Control
• Sequential logic allows the system to remember its current water-level state.
• D flip-flops store the state, while logic determines the next state.
• The clock provides organized state transitions.
• The FSM approach connects directly to how digital control units step through operations.
Monitor → Remember → Decide → Control
19

## Slide 20
THANK YOU
Questions?
Design and Simulation of a Smart Water Tank
20