## Slide 14
13. System Architecture
Sensors
Water availability (U) Full-level condition (S3)
Logic Unit
AND / NOT gates Boolean expressions
Controller
MUX / Decoder Decision logic
Outputs
Pump (P) Alarm (A)
The system moves from sensor inputs through digital logic to final control outputs.
The modular structure makes the design easier to test and expand.

## Slide 15
14. Hardware Components
Water-Level Sensor
Detects water availability and the full-tank condition.
Logic / Controller
Processes the binary sensor
signals.
Pump Driver
Interfaces the control signal
with the pump.
Alarm
Indicates the full-tank condition.
Stable power and correct wiring support reliable operation.
Sensor placement should accurately represent the intended tank levels.

## Slide 16
15. Control Algorithm
1. START
Initialise sensors and outputs.
2. READ
Read U and S3.
3. CHECK
Evaluate the Boolean conditions.
4. ACT
Update Pump and Alarm.
Repeat continuously: read sensors → evaluate logic → update outputs → repeat.
Pump: P = U · S3̅
Alarm: A = S3

## Slide 17
16. Expected Simulation Results
Tank condition | U | S3 | Pump P | Alarm A
No water / sump dry | 0 | 0 | 0 | 0
Water available, not full | 1 | 0 | 1 | 0
Full-level condition | 1 | 1 | 0 | 1
Use these cases as a verification checklist in Logisim/Multisim.
The simulated outputs should match the designed truth table.

## Slide 18
17. Applications, Advantages & Future Scope
Applications
Domestic overhead tanks Apartment water systems Irrigation storage Industrial water management
Advantages
Overflow protection Reduced unnecessary pump operation Simple digital control Easy simulation and verification
Future Scope
Multiple level sensors IoT monitoring Mobile alerts Fault detection and logging
The same digital-logic foundation can be extended to a connected smart-water system.

## Slide 19
18. Conclusion
The project applies CO-2 concepts of combinational logic, Boolean expressions, truth tables, K-Maps, and logic gates .
MUX, decoder comparators demonstrate additional digital design techniques.
ALU and sequential-logic concepts connect the project with other topics in Digital Design and Computer Architecture.
The designed logic provides automatic pump control and overflow alarm based on the water-level conditions.
Simulation and verification confirm that the designed outputs match the required truth table.
The system can be further improved with multiple sensors, IoT monitoring, mobile alerts, and fault detection.